## Slide 1: Detection of road networks in a mid-resolution satellite image
B.Tech Project Presentation
CE495
Nautatava Navlakha (160040007)
Supervisor: Prof. Gopal Patil
Department of Civil Engineering
IIT Bombay

## Slide 2: Outline of the Presentation
1
Road detection
2
Convolutional Neural Networks
3
Motivation and hypothesis
Super resolution
4
Elucidating the mechanism
Our observation
Conclusions
5
6
7

## Slide 3: A brief history
Earlier maps plotted only for areas of spiritual significance or routes to markets.
Transition from paper to digital medium: moving from hand-based mappings to automated maps.
Motivation:
  Transition from manual work to automated work.
  Faster output.
  Capital efficient.
Some of the first road maps in England. http://forums.canadiancontent.net/showthread.php?t=87528
Notes: One of the first road maps in human history. These maps were hand made and were very expensive to maintain. Distances were calculated based on trigonometric angles and approximate measures. Most of these maps only covered important routes, like religious places, or financial and industrial hubs. These maps were rare and expensive. With industrial revolution, maps began to be printed, thus becoming cheaper and affordable. This was the first step towards automation.

## Slide 4: Road detection: Approaching automation
Identifying road networks based on color https://www.mathworks.com/matlabcentral/fileexchange/56234-color-invariant-features-for-object-road-detection
Identifying road networks using SVM based algorithms. https://www.sciencedirect.com/science/article/pii/S2095756416301076#fig4
Road detection by a semi-automatic method with different seed points and Miao algorithm. https://www.sciencedirect.com/science/article/pii/S2095756416301076#fig6
Notes: Other than the simple algorithms depicted, road detection can also be done using fuzzy logics. (Fuzzy logics deal with probabilities rather than definite outcome)

## Slide 5: Convolutional Neural Networks (CNN)
Made up of several convolutional block.
Different types of layers:
  Input layer
  Convolution layer
  Pooling layer (Max pooling, min pooling, mean pooling..)
  Fully connected layer
Different variants of a convolution block:
  Strided convolution
  Dilated Convolution

## Slide 6: CNN Architectures
The way in which the layers are structured and the elements used in each layer determine the architecture of a CNN.
Some architectures: ResNet architecture, encoder-decoders.
ResNet architecture
Encoder-decoders
Skip connection
Image adapted from An encoder-decoder based convolution neural network (CNN) for future advanced driver assistance system (ADAS)
Notes: ResNet: Change In Weighti ∝ ∂ (Error Function) / ∂ (weighti)

## Slide 7: Motivation and hypothesis
Width of roads on a mid-resolution satellite: usually from 1-3 pixels.
Applying road detection algorithms usually skips out the narrow roads.
Road pixel not detected for 1 pixel wide roads?
  Individual pixel-based road-detection algorithm able to identify a road 4 pixel wide.
  Hypothesis: “not able to determine an edge in 1 pixel.”
What if we break every pixel into 4 pixels, then apply edge/road detection algorithms?
  Hypothesis: "Should enhance the road-finding capacity of road-detection model.”
The breaking of every pixel into more pixels is done by super-resolution. Hence the aim of the work is to use SR before applying road-detection.

## Slide 8: Super resolution
Process of upscaling an image.
Enhances the resolution of digital imaging sensors.
Multiple SR algorithms used with different use-cases. Here, need to focus on maximizing signal-to-noise ratio.
Examples of Super-resolution algorithms:
  Decrappify
  Deep Back-Projection Networks (DBPN)
  Enhanced Deep Super-Resolution network (EDSR)
  Wide Activation for Efficient and Accurate Image Super-Resolution (WDSR)
  Very Deep Super-Resolution network (VDSR)
Notes: DBPN has a unique error feedback. error feedback (EF) is usedto guide the reconstruction in the early layer. Here, weanalyze how error feedback can help for better reconstruc-tion. For the scenario without EF, we replace up- and down-projection unit with single up- and down-sampling (decon-volution and convolution) layer.

## Slide 9: Elucidating the mechanism
Image
Super-resolution model
Road-detection model
Road-Network
Model
Input
Output
Notes: Explain the models. Modified resnet coz low-level operation.

## Slide 10: Elucidating the mechanism
Image
Super-resolution model
EDSR
Road-detection model
D-Linknet
Road-Network
Model
Input
Output
We are using EDSR for super-resolution model.
We will be using D-Linknet for road-detection model.
Notes: Explain the models. Modified resnet coz low-level operation.

## Slide 11: Our Observations
The satellite image
Directly applying road-detection
Applying super-resolution before road-detection
Notice how dense our predicted road map is!

## Slide 12: Our Observations
Aerial view
Road Network detected using our model
Road Network detected without super-resolution
This is what happens when model is applied to where it should not be.
Notes: As much as this method looks plausible, it is to be taken care for the model not to be applied on very wide roads.

## Slide 13: Our Observations
Conventional Road detection (without SR)
Road detection with SR
Road detection: fuzzy logic
Using the goodness of both conventional and SR models to create a probability (fuzzy) map.

## Slide 14: Conclusions
Narrow roads that were not recognized by the road-detection model are now visible in the predictions.
Spatial connectivity of broad roads is the cost we pay for the improved prediction.
We can use average out the results of various models to get a fuzzy-algorithm type output to take the best of narrow and broad roads together.
Notes: As much as this method looks plausible, it is to be taken care for the model not to be applied on very wide roads.

## Slide 15: Some unanswered questions based on my work
Small amounts of discontinuities seen when using super-resolution before road-detection.
  Discontinuities due to the fact that noise is an inherent part of super-resolution?
  Any other reason for the discontinuity?
Both road-detection and super-resolution are performed using CNNs. Models are individually trained and together used for prediction. Result is that we get good predictions of narrow road-networks.
  Given that both are CNNs, why are not all roads are identified in the first place?
  Why isn’t super-resolution an inherent part of road-detection?
  Can we make a model combining the power of both SR and road-detection?

## Slide 16: Thank You

## Slide 17: Supplementary material

## Slide 18: Convolution
1
1
0
0
0
1
1
1
0
1
0
0
1
0
1
1
0
0
1
0
0
1
0
0
1
3
3
3
3
2
3
2
3
2
Finding the value of output from a filter
ai,j = f( ∑ ∑Wm,nXm+i,n+j)
1
0
1
1
0
1
1
0
1
(Filter)
(Output matrix)
Input
Go back
Notes: In pooling layer, we find the eigen values.
For strided convolution, we move by more length instead of 1(here).
For dilated convolution, we spread out!

## Slide 19
Conv
ReLU
Conv
xi
xi+1
Modified Residual Block
Conv
Modified Residual Block
Conv
Modified Residual Block
Upsample (4x)
Conv
Upsample (4x)
Conv
Shuffle
Conv
Shuffle
xi
xi+1
Original image
Final image
Conv
Convolution block 3*3
Super-resolution model
EDSR
Go back

## Slide 20
Original image
Conv (7*7, stride =2)
Max Pooling
3*Residual Block
4*Residual Block
6*Residual Block
3*Residual Block
ResNet34 encoder
Max Pooling
Max Pooling
Max Pooling
Conv (3*3, dilation = 1)
Conv (3*3, dilation = 2)
Conv (3*3, dilation = 4)
Conv (3*3, dilation = 8)
Enlarge the receptive Field
Decoder Block
Decoder Block
Decoder Block
Decoder Block
4*4 Transposed Convolution
Conv (3*3, dilation = 1)
Roads in an image
ResNet34 decoder
Road detection model
D-Linknet
Go back

## Slide 21: Dilated convolution